## Slide 1
SOCAMM / SOCAMM2 SLT Yield Issues
Current Drivers, Containment, Actions
Scope: Y6CP 7500MTPS (SOCAMM2 192GB)
Definitions: SLT = HMB1 × QMON | ELC = HMFN × SLT
WW202614 (Apr'26) | Prepared for: Debra Bell, VP

## Slide 2
Executive Snapshot
Current Status
  Y6CP 7500MTPS SOCAMM2: SLT yield at 97.34% — meeting short-term target (97%) but significant gap to long-term target of 99.5% (-2.16%). Continued focus required.
Top Drivers
  • Hung / CPU Thermal issues • Mod-Sys failures (decode limitations) • Blank pre-test failures
What's Improved
  New BIOS implementation enabling better decode and reducing Mod-Sys failures. Retest shows high recoverability on Mod-Sys classified units.

## Slide 3
Quantify the Gap: Y6CP 7500MTPS Yield vs Target
Target Yields (C2 Y6CP 7.5Gbps)
• HMFN Target: 99.00% • SLT Short-term Target: 97.00% (Mar'26+) • SLT Long-term Target: 99.50% • ELC Target: 96.03% (Mar+)
Current Performance (WW202605-WW202614)
• HMFN FY: 98.42% (vs 99.00% target) — Gap: -0.58% • HMB1 FY: 98.42% • QMON FY: 98.90% • SLT FY: 97.34% (vs 97.00% target) — Gap: +0.34% • ELC FY: 95.80% (vs 96.03% target) — Gap: -0.23% Volume: 30,164 units tested at HMFN
Gap to Long-term Target
• SLT at 97.34% — Gap to long-term 99.5% target: -2.16% • Top SLT loss drivers: Hung/CPU Thermal, Mod-Sys, Blank pre-test • HMFN yield gap (-0.58%) also contributing to ELC miss • WW202612 anomaly: HMFN dropped to 65.04% (under investigation)
Source: Module Yield Dashboard - Data as of WW202614

## Slide 4
Primary Driver 1: Hung / CPU Thermal
Root Cause Analysis
• CPU temperature remains high (~90°C) on short engineering test program • Root cause leaning toward equipment-related issue, not test program dependent • Boards under FA lockdown due to elevated CPU temperatures
Ongoing Investigation
• Data collection via IPMI monitoring in progress • Equipment forum investigation ongoing • Thermal solution evaluation underway
Yield Impact
[INSERT FAILCRAWLER DATA: Hung failure contribution to SLT fallout]

## Slide 5
Primary Driver 2: Mod-Sys + Decode Confidence
Key Challenge: Decode Limitation
• Mod-Sys failures indicate system-level issues with limited decode capability • Current BIOS encryption limits failure analysis depth • System-to-DQ mapping needed for accurate failure attribution
BIOS Improvement
• New BIOS implementation enabled to ensure failures are decoded correctly • Encryption-disabled BIOS enables deeper debugging • Improved system-to-DQ mapping for accurate failure classification
Retest Results
• Retest shows high recoverability on Mod-Sys classified units • Ongoing deep dive to quantify true DRAM vs system failures • [INSERT: Mod-Sys retest pass rate from FAILCRAWLER analysis]

## Slide 6
Containment, Owners & Executive Asks
Containment Actions
• Taskforce ongoing to address yield impact • Pre-testing issue investigation active • New BIOS deployment in progress • Thermal monitoring enhanced
Action Owners
• Hung/Thermal: [Equipment Team] • Mod-Sys/Decode: [BIOS/Debug Team] • Blank Pre-test: [Test Engineering] • Tracking/DOE: [Yield Engineering]
Executive Asks
1. Equipment team resource prioritization for thermal root cause 2. Expedited BIOS release approval for decode improvement 3. Cross-functional alignment on Mod-Sys classification criteria
Target Timeline
• Thermal RC: +2 weeks • New BIOS deployment: +1 week • Yield target achievement: [TBD based on RC]