## Slide 1
No-Boot Failure Analysis
SOCAMM / SOCAMM2 Module Debug Summary
April 27, 2026

## Slide 2
Executive Summary
Jira | DID | Module | Failure Mode | Root Cause | Status
MMPTESTPROC-1969 | Y62P | SOCAMM | CONT @ U4 | LP1C_CA3, LP1C_WCLK0_N | De-pop/Reball
MMPTESTPROC-1866 | Y63N | SOCAMM2 | DQ @ U2 | DQ6 (U2D2), DQ1 (U2D0) | pFA Submitted
MMPTESTPROC-1951 | Y6CP | SOCAMM2 | No Boot @ HMB1 | TBD | Awaiting Retest
Key Findings:
• No Boot failures don't generate test summaries - tracked via Jira only
• HMFN Pass + HMB1 No Boot = stress-related marginal defect (not parametric)
• Single DQ/signal failures suggest localized defects (solder, via, trace)
• Use mfm +failcrawler for detailed DQ/address-level analysis
• PCB schematic trace essential for identifying common die
PCB References:
• SOCAMM (Y62P): PCB 3928 - 694 ball, 16-layer
• SOCAMM2 (Y63N, Y6CP): PCB 3957 - 315 ball, 16-layer

## Slide 3
Case 1: Y62P SOCAMM - 56A76459 (MMPTESTPROC-1969)
Timeline:
• Time 0: ROW failure at HMB1 Production
• ENG Retest: Module did not boot up
• VI: Gold plate contamination observed
• HMFN Rerun: FAIL (1st CONT, 2nd SPD)
• HMFN Retest: Passed 1/5 rounds (intermittent)
Failure Analysis:
• Time 0: Single FID FUNC 3 failure
• FID: 755088L:22:P08:15 (U4D2)
• Retest: 3/5 rounds SBIN 20 CONT failure
• Failing signals: LP1C_CA3, LP1C_WCLK0_N
• Both signals route to U4
Conclusion:
• Likely U4 die/solder issue
• Proceeding with de-pop and re-ball
SOCAMM Module (PCB 3928) - U4 Highlighted
+----------+-----------+-------------+ | U1 | U2 | Passives | | SC 0,1 | SC 2,3 | | +----------+-----------+-------------+ | U3 | ** U4 ** | PMIC | | SC 4,5 | SC 6,7 | | | | LP1C/1D | | +----------+-----------+-------------+ ^ LP1C_CA3 & LP1C_WCLK0_N
Status: De-pop & Re-ball in Progress

## Slide 4
Case 2: Y63N SOCAMM2 - 569D40EE & 569D4898 (MMPTESTPROC-1866)
Timeline:
• HMFN PROD: PASS (03-05-2026)
• HMB1 PROD: FAIL SBIN 3;3 DQ (03-21-2026)
• HMB1 ENG: NO BOOT (no summary)
• HMFN ENG: PASS (04-08-2026)
Key Insight:
Passed HMFN twice = No parametric issue
Problem is HMB1-specific (stress/timing)
Failure Details:
• 569D40EE: U2D2, DQ6, SYS_ODD_BURST_BIT
• 569D4898: U2D0, DQ1, MULTI_HALFBANK_SINGLE_DQ
• DRAMFAIL=NO (system classification)
• Single DQ line failure per module
Field | 569D40EE | 569D4898
ULOC | U2D2 | U2D0
DQ Line | DQ6 | DQ1
Signal | LPDDR0C_DQ0[6] | LPDDR0C_DQ0[1]
Die Pin | E6 | E2
Status: pFA Submitted MMPTESTPROC-1970, GELLA-28385

## Slide 5
Case 2: Y63N - pFA Request Details
pFA Focus Areas:
1. Thermal Imaging - U2 region hot spots
2. IV Curve Tracing - DQ6 & DQ1 signal paths
3. X-ray (if needed) - Solder joints at U2
4. Cross-section (if IV shows anomaly)
Probe Points:
• Die bump -> PCB via -> Socket pin
• 569D40EE: LPDDR0C_DQ0[6] at pin E6
• 569D4898: LPDDR0C_DQ0[1] at pin E2
Suspected Failure Mechanism:
• Cracked/marginal solder joint at U2
• Via defect in DQ signal path
• Delamination at die-to-substrate interface
• Passes HMFN but fails under HMB1 stress
SOCAMM2 Module (PCB 3957) - U2 Highlighted
+-------+--------+-------+-------+---------+ | U1 | ** U2**| U3 | U4 | PMIC | | SC0,1 | SC2,3 | SC4,5 | SC6,7 | | | LPDDR | LPDDR | | | | | 0A/B | 0C/0D | | | | | | DQ6,DQ1| | | | +-------+--------+-------+-------+---------+
Related Jira Tickets:
* MMPTESTPROC-1866 - Retest Request
* MMPTESTPROC-1970 - pFA Request
* GELLA-28385 - Module Collection

## Slide 6
Case 3: Y6CP SOCAMM2 - 5764B16E & 5764B46E (MMPTESTPROC-1951)
Status: Awaiting Retest
Timeline:
• Time 0: No Boot at HMB1
• SOL log collected - MOBO booted during collection
• Unable to collect Good SOL log (DEMQRA issue)
• Gold plate contamination noted in lot history
Current Activity:
• Running HMFN 2X + HMB1 1X
• Test loading: 1 BAD module + 3 KGM
• FA team executing retest
Pending:
• Retest results from FA team
• Good SOL log for comparison
• TSE support for production system loan
MSN | Failure | Observation
5764B16E | No Boot @ HMB1 | Gold plate contamination
5764B46E | No Boot @ HMB1 | Gold plate contamination
Status: Awaiting Retest Results

## Slide 7
No-Boot Debug Methodology
Debug Workflow: 1. Check Module History mhist <MSN1> <MSN2> -sbin -> Identify failure progression and SBINs 2. Get Production Failure Details frpt -xf <SUMMARY> -mod_id=/<MSN>/ +# -quick=/summary,mod_id/ +module -> Failed register, test pattern 3. Run ENG Retest (HMFN + HMB1) -> HMFN Pass + HMB1 No Boot = stress-related marginal defect -> Note: No Boot = No Summary (track via Jira) 4. Check HMFN ENG Test Details tdat <HMFN_ENG_SUMMARY> -> Verify ddpcont#, shorts#, vr_power_good passed 5. Get Detailed Failure Analysis mfm <MSN1> <MSN2> -step=<step> +failcrawler -> ULOC, DQ line, ROW/COL pattern, FAILCRAWLER category 6. Trace Signal to Die (PCB Schematic) -> PCB 3928 (SOCAMM), PCB 3957 (SOCAMM2) -> Multiple signals on same die = die/solder issue 7. Submit pFA Request -> Thermal imaging, IV curve, X-ray -> Specify exact signal and pin locations

## Slide 8
Next Steps & Summary
Case | DID | Next Action | Owner | Target
MMPTESTPROC-1969 | Y62P | Complete de-pop/reball, evaluate U4 | FA Team | TBD
MMPTESTPROC-1866 | Y63N | pFA thermal + IV curve | pFA Team | TBD
MMPTESTPROC-1951 | Y6CP | Await retest results | FA Team | TBD
Summary:
• 3 No-Boot cases under investigation across Y62P, Y63N, Y6CP
• Common pattern: failures localized to specific die/DQ lines
• HMFN parametric tests pass -> stress-related marginal defects
• Gold plate contamination observed in multiple cases
Key Learnings:
• mfm +failcrawler provides critical DQ-level failure details
• PCB schematic trace essential for root cause identification
• pFA (thermal + IV) needed to locate marginal defects