## Slide 1: Y6CP FID DPM Recovery Analysis
Month 04 2025
Abbiramavali
MMP DEG PE
READ & DELETE BEFORE USING
Presentation titles should be three lines maximum. If presentation title cannot be rewritten to fit on three lines, text size should be reduced to fit on three lines. Text size may be increased for very short titles.

## Slide 2: Executive Summary
Key Findings (SOCAMM2 7500MT, 10-Week Cumulative): HMB1 Step: • Yield: 98.32% (29,788 modules tested) • Total FID DPM: 265.7 → Remaining: 98.6 DPM • Recovery: 167.2 DPM (63% recoverable) QMON Step: • Yield: 98.79% (24,126 modules tested) • Total FID DPM: 191.2 → Remaining: 59.4 DPM • Recovery: 131.8 DPM (69% recoverable) Combined SLT (HMB1 × QMON): • Combined Yield: 97.13% • Total FID DPM: 456.9 → Remaining: 157.9 DPM • Total Recoverable: 298.9 DPM (65%)
SOCAMM2 7500MT | WW202606-15 (10 Weeks) HMB1 & QMON Steps

## Slide 3: DPM to MFG View: Bridging the Communication Gap
Metric | HMB1 | QMON | Combined SLT
MFG View (Yield %) | 98.32% | 98.79% | 97.13%
Modules Tested | 29,788 | 24,126 | -
Modules Failed | 500 | 292 | 792
ENG View (FID DPM) | 265.7 | 191.2 | 456.9
Recoverable DPM | 167.2 | 131.8 | 298.9
Remaining DPM | 98.6 | 59.4 | 157.9
Key Message: MFG sees 97.1% yield (meeting shipping targets), but ENG sees 456.9 FID DPM total risk. Through BIOS/HW+SOP recovery mechanisms, we reduce Remaining risk to 157.9 FID DPM.

## Slide 4: DPM Calculation Method
Formula: Unique Failing MSNs FID DPM = ─────────────────────────── × 1,000,000 Total FID UIN Calculation: HMB1: FID DPM = 500 unique failing modules / 1,881,631 total FIDs × 1,000,000 = 265.73 DPM QMON: FID DPM = 292 unique failing modules / 1,527,576 total FIDs × 1,000,000 = 191.15 DPM Key Points: • Numerator: Count of unique MSNs (modules) with failures - each module counted ONCE • Denominator: Total FID UIN (component population) from mtsums +fidag • This gives component-level perspective while counting module-level failures

## Slide 5: Top FAILCRAWLER Categories by DPM
HMB1 (Total: 265.7 DPM) ─────────────────────────────────── • MULTI_BANK_MULTI_DQ: 98.0 DPM (37%) • SINGLE_BURST_SINGLE_ROW: 46.3 DPM (17%) • HGDC: 41.6 DPM (16%) • HANG: 15.9 DPM (6%) • SYS_EVEN_BURST_BIT: 12.8 DPM (5%) • MULTI_HALFBANK_SINGLE_DQ: 8.7 DPM (3%) • UNKNOWN: 7.4 DPM (3%) • MULTI_HALFBANK_MULTI_DQ: 6.2 DPM (2%)
QMON (Total: 191.2 DPM) ─────────────────────────────────── • MULTI_BANK_MULTI_DQ: 105.5 DPM (55%) • SINGLE_BURST_SINGLE_ROW: 25.3 DPM (13%) • HGDC: 7.6 DPM (4%) • SYS_EVEN_BURST_BIT: 6.9 DPM (4%) • ROW: 6.1 DPM (3%) • DB: 6.0 DPM (3%) • MULTI_HALFBANK_SINGLE_DQ: 5.0 DPM (3%) • MULTI_HALFBANK_MULTI_DQ: 4.7 DPM (2%)

## Slide 6: Recovery Type Assignments
Recovery Mechanism Mapping: ┌─────────────────────────────────────────────────────────────────────────┐ │ BIOS 100% Recovery (Full recovery projected) │ │ • MULTI_BANK_MULTI_DQ - Multi-bank failures recoverable via BIOS │ ├─────────────────────────────────────────────────────────────────────────┤ │ BIOS 50% Recovery (Partial recovery projected) │ │ • SINGLE_BURST_SINGLE_ROW, HGDC, SYS_EVEN_BURST_BIT │ │ • SYS_ODD_BURST_BIT, MULTI_BANK_2ROW, SECTION_FAIL_PERIPH │ ├─────────────────────────────────────────────────────────────────────────┤ │ HW+SOP 100% Recovery (Hardware/SOP fixes) │ │ • HANG - System hang recoverable via hardware/SOP improvements │ ├─────────────────────────────────────────────────────────────────────────┤ │ RPx 0% Recovery (Verified - No false fails found) │ │ • MULTI_HALFBANK_*, ROW, ROW_LOCAL, MULTI_BANK_SINGLE_DQ │ │ • Note: socamm_false_miscompare.py verified 0% false fail rate │ ├─────────────────────────────────────────────────────────────────────────┤ │ No Recovery (True failures - Remaining) │ │ • SB, DB, UNKNOWN, BOOT, SB_MODSYS, SINGLE_BANK, COL_FUSE │ └─────────────────────────────────────────────────────────────────────────┘ Note: ROW MSN_STATUS does NOT get BIOS recovery - only RPx can recover ROW failures

## Slide 7: Recovery Summary by Step

## Slide 8
478.0
Total FID DPM
-229.6
BIOS 100%
-93.5
BIOS 50%
-18.0
HW+SOP
0
RPx
136.9
Remaining
Total FID DPM
Recovery
Remaining
Total Recovery: 71.4% (341.1 DPM recovered)

## Slide 10: Appendix: Data Sources & Commands
Data Collection: 1. Unique Failing MSNs (Numerator): mtsums -dbase=y6cp -step={step} -module_form_factor=socamm2 \ -module_speed=7500MTPS -mfg_workweek=202608,...,202617 +stdf +msnag 2. Total FID UIN (Denominator): mtsums -dbase=y6cp -step={step} -module_form_factor=socamm2 \ -module_speed=7500MTPS -mfg_workweek=202608,...,202617 +stdf +fidag 3. FAILCRAWLER Breakdown: mtsums ... +stdf +fm +fc 4. MSN_STATUS × FAILCRAWLER Correlation: mtsums ... +stdf +msnag -format=/msn_status,failcrawler/ 5. RPx Verification: /home/nmewes/Y6CP_FA/socamm_false_miscompare.py --sums {slash_paths} Result: 0% false fail rate verified Data Scope: • Product: SOCAMM2 7500MTPS • Period: WW202606-202615 (10 weeks cumulative) • Steps: HMB1, QMON • Database: y6cp

## Slide 11
READ & DELETE BEFORE USING
If needed, update the legal notice on the end slide using View > Slide Master. When done, View > Normal.
Both the “End Slide” and “End Slide – Dark Mode” slide masters should be updated consistently.