## Slide 1
Y6CP cDPM Recovery Analysis
SOCAMM2 7500MT | WW202608-17 (10 Weeks) HMB1 & QMON Steps

## Slide 2
Executive Summary
Key Findings (SOCAMM2 7500MT, 10-Week Cumulative): HMB1 Step: • Yield: 98.32% (29,788 modules tested) • Total cDPM: 265.7 → Customer-Facing: 98.6 DPM • Recovery: 167.2 DPM (63% recoverable) QMON Step: • Yield: 98.79% (24,126 modules tested) • Total cDPM: 191.2 → Customer-Facing: 59.4 DPM • Recovery: 131.8 DPM (69% recoverable) Combined SLT (HMB1 × QMON): • Combined Yield: 97.13% • Total cDPM: 456.9 → Customer-Facing: 157.9 DPM • Total Recoverable: 298.9 DPM (65%)

## Slide 3
MFG vs ENG View: Bridging the Communication Gap
Metric | HMB1 | QMON | Combined SLT
MFG View (Yield %) | 98.32% | 98.79% | 97.13%
Modules Tested | 29,788 | 24,126 | -
Modules Failed | 500 | 292 | 792
ENG View (cDPM) | 265.7 | 191.2 | 456.9
Recoverable DPM | 167.2 | 131.8 | 298.9
Customer-Facing DPM | 98.6 | 59.4 | 157.9
Key Message: MFG sees 97.1% yield (meeting shipping targets), but ENG sees 456.9 cDPM total risk. Through BIOS/HW+SOP recovery mechanisms, we reduce customer-facing risk to 157.9 cDPM.

## Slide 4
DPM Calculation: Kevin Roos Method
Formula: Unique Failing MSNs cDPM = ─────────────────────────── × 1,000,000 Total FID UIN Calculation: HMB1: cDPM = 500 unique failing modules / 1,881,631 total FIDs × 1,000,000 = 265.73 DPM QMON: cDPM = 292 unique failing modules / 1,527,576 total FIDs × 1,000,000 = 191.15 DPM Key Points: • Numerator: Count of unique MSNs (modules) with failures - each module counted ONCE • Denominator: Total FID UIN (component population) from mtsums +fidag • This gives component-level perspective while counting module-level failures

## Slide 5
Top FAILCRAWLER Categories by DPM
HMB1 (Total: 265.7 DPM) ─────────────────────────────────── • MULTI_BANK_MULTI_DQ: 98.0 DPM (37%) • SINGLE_BURST_SINGLE_ROW: 46.3 DPM (17%) • HGDC: 41.6 DPM (16%) • HANG: 15.9 DPM (6%) • SYS_EVEN_BURST_BIT: 12.8 DPM (5%) • MULTI_HALFBANK_SINGLE_DQ: 8.7 DPM (3%) • UNKNOWN: 7.4 DPM (3%) • MULTI_HALFBANK_MULTI_DQ: 6.2 DPM (2%)
QMON (Total: 191.2 DPM) ─────────────────────────────────── • MULTI_BANK_MULTI_DQ: 105.5 DPM (55%) • SINGLE_BURST_SINGLE_ROW: 25.3 DPM (13%) • HGDC: 7.6 DPM (4%) • SYS_EVEN_BURST_BIT: 6.9 DPM (4%) • ROW: 6.1 DPM (3%) • DB: 6.0 DPM (3%) • MULTI_HALFBANK_SINGLE_DQ: 5.0 DPM (3%) • MULTI_HALFBANK_MULTI_DQ: 4.7 DPM (2%)

## Slide 6
Recovery Type Assignments
Recovery Mechanism Mapping: ┌─────────────────────────────────────────────────────────────────────────┐ │ BIOS 100% Recovery (Full recovery projected) │ │ • MULTI_BANK_MULTI_DQ - Multi-bank failures recoverable via BIOS │ ├─────────────────────────────────────────────────────────────────────────┤ │ BIOS 50% Recovery (Partial recovery projected) │ │ • SINGLE_BURST_SINGLE_ROW, HGDC, SYS_EVEN_BURST_BIT │ │ • SYS_ODD_BURST_BIT, MULTI_BANK_2ROW, SECTION_FAIL_PERIPH │ ├─────────────────────────────────────────────────────────────────────────┤ │ HW+SOP 100% Recovery (Hardware/SOP fixes) │ │ • HANG - System hang recoverable via hardware/SOP improvements │ ├─────────────────────────────────────────────────────────────────────────┤ │ RPx 0% Recovery (Verified - No false fails found) │ │ • MULTI_HALFBANK_*, ROW, ROW_LOCAL, MULTI_BANK_SINGLE_DQ │ │ • Note: socamm_false_miscompare.py verified 0% false fail rate │ ├─────────────────────────────────────────────────────────────────────────┤ │ No Recovery (True failures - customer-facing) │ │ • SB, DB, UNKNOWN, BOOT, SB_MODSYS, SINGLE_BANK, COL_FUSE │ └─────────────────────────────────────────────────────────────────────────┘ Note: ROW MSN_STATUS does NOT get BIOS recovery - only RPx can recover ROW failures

## Slide 7
Recovery Summary by Step
Recovery Type | HMB1 DPM | QMON DPM | Combined | Rate
BIOS 100% | 98.0 | 105.5 | 203.5 | 100%
BIOS 50% | 53.2 | 25.6 | 78.8 | 50%
HW+SOP | 15.9 | 0.7 | 16.6 | 100%
RPx (Verified) | 0.0 | 0.0 | 0.0 | 0%
Total Recovered | 167.2 | 131.8 | 298.9 | -
No Recovery | 41.3 | 30.9 | 72.2 | 0%
Customer-Facing | 98.6 | 59.4 | 157.9 | -

## Slide 8
456.9
Total cDPM
-203.5
BIOS 100%
-78.8
BIOS 50%
-16.6
HW+SOP
0
RPx
157.9
Customer Facing
Total cDPM
Recovery (Decrease)
Customer-Facing
Total Recovery: 65.4% (298.9 DPM recovered)

## Slide 9
Appendix: Data Sources & Commands
Data Collection: 1. Unique Failing MSNs (Numerator): mtsums -dbase=y6cp -step={step} -module_form_factor=socamm2 \ -module_speed=7500MTPS -mfg_workweek=202608,...,202617 +stdf +msnag 2. Total FID UIN (Denominator): mtsums -dbase=y6cp -step={step} -module_form_factor=socamm2 \ -module_speed=7500MTPS -mfg_workweek=202608,...,202617 +stdf +fidag 3. FAILCRAWLER Breakdown: mtsums ... +stdf +fm +fc 4. MSN_STATUS × FAILCRAWLER Correlation: mtsums ... +stdf +msnag -format=/msn_status,failcrawler/ 5. RPx Verification: /home/nmewes/Y6CP_FA/socamm_false_miscompare.py --sums {slash_paths} Result: 0% false fail rate verified Data Scope: • Product: SOCAMM2 7500MTPS • Period: WW202608-202617 (10 weeks cumulative) • Steps: HMB1, QMON • Database: y6cp