## Slide 1
Module Yield Dashboard
Weekly Yield Tracking for SOCAMM/SOCAMM2 Modules HMFN | HMB1 | QMON Test Steps

## Slide 2
Dashboard Overview
• Real-time yield monitoring for SOCAMM and SOCAMM2 modules
• Data sourced from frpt and mtsums commands
• Five main analysis tabs:
◦ Yield Analysis - Weekly trends, bin distribution, heatmaps
◦ Module ELC Yield - HMFN, SLT, ELC with target lines
◦ Pareto Analysis - Register fallout and FAILCRAWLER DPM
◦ Fail Viewer - FID-level fail analysis
◦ Machine Trend Analysis - SMT6 tester and GRACE monitoring
• Accessible via: http://bolpedh03.micron.com:8502

## Slide 3
Global Filters (Sidebar)
• Design ID (DID) - Y6CP, Y62P, Y63N, Y42M, etc.
• Module Form Factor - SOCAMM, SOCAMM2
• Module Density - 48GB, 96GB, 128GB, 192GB, 256GB
• Module Speed - 7500MTPS, 8000MTPS, 9600MTPS
• Test Facility - PENANG, BOISE, or All
• Work Week Range - Start and end work week selection
• Cache Control - Enable/disable query caching

## Slide 4
Tab 1: Yield Analysis
Weekly Yield Trends
• Line chart with yield % over work weeks
• Paired volume bars (UIN) for context
• Series selector for DID/Step combinations
• Adjustable Y-axis minimum (0-99%)
• Fiscal month labels on X-axis
• Target lines (HMFN: 99%, SLT: 97%, ELC: 96%)
Additional Charts
• Bin Distribution - Stacked bar by work week
• Density Heatmap - Yield by density x week
• Speed Heatmap - Yield by speed x week
• WW Summary Cards - DID breakdown with sparklines
• Animated gauge charts (toggle view)

## Slide 5
Tab 2: Module ELC Yield
Yield Flow Visualization
• HMFN -> SLT -> ELC yield progression
• SLT = HMB1 x QMON (calculated)
• ELC = HMFN x SLT (calculated vs actual)
• 4-week rolled yields for trend analysis
• Delta indicators (calculated vs actual)
Target Lines
• HMFN Target: 99% (blue dotted)
• SLT Target: 96.5% -> 97% (stepped, red)
• ELC Target: Schedule-based (green)
• Long-term SLT Target: 99.5%
• Color-coded status (green/yellow/red)

## Slide 6
Tab 3: Pareto Analysis
Register Fallout (Sub-tab 1)
• Top 5 failed registers by test step
• Breakdown by DID, form factor, speed, density
• Work week trend analysis
• Fallout percentage ranking
FAILCRAWLER DPM (Sub-tab 2)
• Live mtsums data fetch
• FAILCRAWLER category breakdown
• MSN_STATUS correlation heatmap
• Ranked table with MDPM and cDPM
• Latest WW vs Cumulative toggle

## Slide 7
MDPM and cDPM Metrics
• MDPM (Module Defects Per Million)
◦ Formula: (Unique Modules / Total MUIN) x 1M
◦ Example: 4 modules / 5,683 total = 703.85 MDPM
• cDPM (Component Defects Per Million)
◦ Formula: (Unique FIDs / Total Component UIN) x 1M
◦ Example: 256 FIDs / 342,201 total = 748.10 cDPM
• Both use TOTAL population as denominator
• MSN_STATUS Ranked Table columns:
◦ Rank, MSN_STATUS, Modules, MDPM, FIDs, cDPM, Contrib %, Cumul %

## Slide 8
Tab 4: Fail Viewer
• FID-level failure analysis and visualization
• Decoder support by Design ID:
◦ Y62P - Full decoder support
◦ Y6CP - Full decoder support
◦ Y63N - Uses Y6CP baseline decoder
◦ Y42M - Simplified decoder
• Interactive failure pattern exploration
• MSN (Module Serial Number) lookup
• Component-level fail details

## Slide 9
Tab 5: Machine Trend Analysis
SMT6 Tester Yield
• Socket & Site yield analysis
• Site encoding: S#C#P## format
• Physical socket (P##) monitoring
• Trend classification by machine
• Click machine -> Socket health grid
• Channel detail view for diagnostics
GRACE Motherboard Monitoring
• NVGRACE machine health (HMB1/QMON)
• Hang cDPM by machine chart
• Week-over-week comparison
• Status: New Issue / Fixed / Recurring
• Drill-down for 100% fail cases
• Row highlighting for alerts

## Slide 10
Data Sources & Commands
frpt Command
• Yield data with -myquick grouping
• Parameters: step, form_factor, dbase
• Workweek range filtering
• Facility selection (Penang/Boise)
• Returns: UIN, UPASS, YIELD %
mtsums Command
• FAILCRAWLER data with +fc flag
• MSN_STATUS correlation with +msnag
• FID-level data with +fid flag
• Component UIN with +fidag flag
• Fail Mode cDPM with +fm flag

## Slide 11
Technical Architecture
• Backend: Python 3.11 + Streamlit
• Visualization: Plotly (interactive charts)
• Data Processing: Pandas DataFrames
• Deployment: systemd user service (auto-restart)
• Port: 8502 (HTTP)
• Session State: Caching for performance

## Slide 12
Key Features Summary
• Real-time yield monitoring across multiple test steps
• Interactive filters for DID, density, speed, facility
• Target line visualization with stepped schedules
• MDPM and cDPM metrics with total population denominator
• MSN_STATUS correlation analysis
• Machine-level yield monitoring (SMT6, GRACE)
• Week-over-week trend comparisons
• Automated service with auto-restart capability

## Slide 13
Questions?
Dashboard URL: http://bolpedh03.micron.com:8502 Module Yield Dashboard v1.0