## Slide 1
Y6CP cDPM Recovery Analysis
10-Week Cumulative Analysis | WW2608-17

## Slide 2
Executive Summary
Metric | HMB1 | QMON | Combined SLT
Volume (MUIN) | 30,528 | 24,940 | 55,468
Total cDPM (Kevin) | 266.08 | 192.11 | 458.19
Recovered DPM | 149.95 | 125.88 | 275.83
Customer-Facing DPM | 116.13 | 66.23 | 182.37
Key Findings:
• 10-week cumulative volume: 55,468 modules (WW2608-17)
• Combined SLT yield: 98.54%
• Kevin's cDPM: (Unique failing MSNs / Total FIDs) × 1M
• RPx rates (Verified): HMB1=0.0%, QMON=0.0%
• Top DPM: MULTI_BANK_MULTI_DQ (BIOS 100% recoverable)
• Customer-facing DPM after recovery: 182.37

## Slide 3
MSN_STATUS × FAILCRAWLER Correlation
MSN_STATUS | FAILCRAWLER | DPM | Recovery | Rate
Mod-Sys | MULTI_BANK_MULTI.. | 90.4 | BIOS 100% | 100%
Mod-Sys | HGDC | 39.5 | RPx✓ | 0.0%
Mod-Sys | SINGLE_BURST_SIN.. | 31.6 | BIOS 50% | 50%
Hang | HANG | 15.7 | HW+SOP | 100%
Row | SINGLE_BURST_SIN.. | 14.1 | RPx✓ | 0.0%
DQ | SYS_EVEN_BURST_BIT | 7.8 | BIOS 50% | 50%
Mod-Sys | MULTI_HALFBANK_M.. | 6.6 | BIOS 50% | 50%
Mod-Sys | UNKNOWN | 6.2 | RPx✓ | 0.0%
SB_Int | SB | 5.2 | No Recovery | 0.0%
Multi-DQ | MULTI_BANK_MULTI.. | 5.2 | BIOS 100% | 100%
■ HMB1 (DPM: 266.08, RPx✓=0.0%)
MSN_STATUS | FAILCRAWLER | DPM | Recovery | Rate
Mod-Sys | MULTI_BANK_MULTI.. | 96.8 | BIOS 100% | 100%
Row | SINGLE_BURST_SIN.. | 14.1 | RPx✓ | 0.0%
Mod-Sys | SINGLE_BURST_SIN.. | 10.9 | BIOS 50% | 50%
Mod-Sys | HGDC | 7.5 | RPx✓ | 0.0%
Multi-DQ | MULTI_BANK_MULTI.. | 6.4 | BIOS 100% | 100%
Mod-Sys | ROW | 5.0 | RPx✓ | 0.0%
Mod-Sys | MULTI_HALFBANK_M.. | 4.6 | BIOS 50% | 50%
SB_Int | SB | 4.5 | No Recovery | 0.0%
DQ | SYS_EVEN_BURST_BIT | 4.5 | BIOS 50% | 50%
DQ | MULTI_HALFBANK_S.. | 4.5 | BIOS 50% | 50%
■ QMON (DPM: 192.11, RPx✓=0.0%)
Recovery Legend: BIOS 100%=MULTI_BANK_MULTI_DQ | BIOS 50%=BANK/BURST/PERIPH | HW+SOP=Hang | RPx✓=Verified false fails | No Recovery=SB/DB
RPx Verified: HMB1=44,515 screened, 0 false fails | QMON=84,340 screened, 1 false fails

## Slide 4
Recovery Summary by Type
Recovery Type | DPM | Rate | Recovered DPM
BIOS 100% | 96.66 | 100% | 96.66
BIOS 50% | 72.14 | 50% | 36.07
RPx✓ | 69.96 | 0.0%✓ | 0.00
HW+SOP | 17.22 | 100% | 17.22
No Recovery | 10.11 | 0% | 0.00
TOTAL | 266.08 |  | 149.95
■ HMB1 → Customer-Facing: 116.13 DPM
Recovery Type | DPM | Rate | Recovered DPM
BIOS 100% | 103.21 | 100% | 103.21
BIOS 50% | 44.05 | 50% | 22.02
RPx✓ | 33.52 | 0.0%✓ | 0.00
No Recovery | 10.67 | 0% | 0.00
HW+SOP | 0.64 | 100% | 0.64
TOTAL | 192.11 |  | 125.88
■ QMON → Customer-Facing: 66.23 DPM
Kevin's DPM & RPx Verification:
• cDPM = (Unique Failing MSNs / Total FIDs) × 1,000,000
• RPx Verification: Used socamm_false_miscompare.py on 128,855 total failures
• HMB1: 0/44,515 verified false fails = 0.00%
• QMON: 1/84,340 verified false fails = 0.00%
• Customer-Facing = Total DPM - (BIOS + HW+SOP + Verified RPx)

## Slide 5
cDPM Methodology (Kevin Roos)
Kevin Roos DPM Formula:
cDPM = (Unique Failing MSNs / Total FIDs) × 1,000,000
• Numerator: Count each failing MODULE once
• Denominator: Total FID count across all tested modules
Recovery Types:
1. BIOS 100%: MULTI_BANK_MULTI_DQ → Full BIOS recovery
2. BIOS 50%: BANK/BURST/PERIPH patterns → Partial BIOS
3. HW+SOP: Hang MSN_STATUS → 100% hardware fix
4. RPx✓: VERIFIED false fail rate from socamm_false_miscompare.py
5. No Recovery: SB/DB FAILCRAWLERs → DRAM defects
RPx Verification Process:
• Run socamm_false_miscompare.py --sums <SLASH_paths>
• Excludes Hang & Boot (no fail addresses to screen)
• Returns actual verified false fail count
• Rate = False Fails / Total Screened
ROW MSN_STATUS Rule:
ROW failures do NOT get BIOS recovery
Even SINGLE_BURST_SINGLE_ROW → only RPx applies
Rationale: Row-level = potential DRAM issue