## Slide 1
Y6CP SLT cDPM Recovery Analysis
HMB1 & QMON | WW202613-15 | Penang
April 23, 2026

## Slide 2
DPM Calculation Methodology
DPM Formula (Kevin Roos Method): DPM = (Unique Failing MSNs / Total FIDs) × 1,000,000 Yield Calculation (Module-Based): Actual Yield = (Passing Modules / Total Modules) × 100 Yield Recovery = (Recovered MSNs / Total MUIN) × 100 Recovery Priority: HW+SOP → No Recovery (SB/DB) → BIOS 100% → BIOS 50% → RPx → No Recovery (Row) Key Rules: • SB/DB FAILCRAWLERs = actual bit errors → No recovery possible • ROW MSN_STATUS never gets BIOS (even with BURST patterns) → Only RPx can recover • BIOS 100%: MULTI_BANK_MULTI_DQ FAILCRAWLER • BIOS 50%: BANK/BURST/PERIPH patterns in FAILCRAWLER name

## Slide 3
Executive Summary
Key Findings (WW202613-15): • Volume Tested: - HMB1: 11,907 modules (217 failed) - QMON: 7,888 modules (100 failed) • Actual SLT Yield: - HMB1: 98.18% | QMON: 98.73% - Combined SLT: 96.93% • cDPM Overview: - HMB1: 364 DPM total → 12 DPM customer-facing - QMON: 286 DPM total → 20 DPM customer-facing • Recovery Impact: - HMB1: +1.73% yield gain | QMON: +1.05% yield gain - Combined SLT Projected: 99.70% (+2.76%)

## Slide 4
DPM Waterfall: Total DPM → Customer-Facing DPM (WW202613-15)
HMB1
364
Total DPM
-212
-BIOS
-121
-HW+SOP
12
Customer Facing
QMON
286
Total DPM
-189
-BIOS
20
Customer Facing
Waterfall bridges MFG view (Total DPM) to Customer view (Customer-Facing DPM): • Green = DPM recovered | Blue = Totals • HMB1: 364 → 12 DPM (recovered: 334) • QMON: 286 → 20 DPM (recovered: 189)

## Slide 5
SLT Yield Waterfall: Current → Projected (WW202613-15)
Combined SLT Yield
97
Current Yield
+2
+HMB1
+1
+QMON
100
Projected Yield
Bridging Yield and DPM: • Current SLT Yield: 96.93% (HMB1 98.18% × QMON 98.73%) • Recovery: HMB1 +1.73% | QMON +1.05% • Projected SLT Yield: 99.70% | Improvement: +2.76%

## Slide 6
Recovery Summary
Step | Total DPM | BIOS | HW+SOP | No Recovery | Customer-Facing
HMB1 | 364 | 212 | 121 | 18 | 12
QMON | 286 | 189 | 0 | 78 | 20
Recovery Breakdown: • BIOS (100%): MULTI_BANK_MULTI_DQ timing fix - Combined: 401 DPM recoverable • HW+SOP (100%): Hang failures - hardware + SOP fix - HMB1: 121 DPM • No Recovery (DRAM-related): SB/DB FAILCRAWLERs, ROW MSN_STATUS - Combined: 96 DPM (actual silicon issues) • Customer-Facing cDPM: 32 DPM total

## Slide 7
SLT Yield Impact Summary
Step | Volume | Actual Yield | Yield Gain | Projected Yield
HMB1 | 11,907 | 98.18% | +1.73% | 99.91%
QMON | 7,888 | 98.73% | +1.05% | 99.79%
Combined SLT | - | 96.93% | +2.76% | 99.70%
Key Takeaways: • Current SLT Yield: 96.93% → Projected: 99.70% • BIOS timing fix is the largest recovery opportunity (401 DPM combined) • Customer-Facing cDPM after all recovery: 32 DPM - HMB1: 12 DPM | QMON: 20 DPM • No Recovery failures (DRAM-related): 96 DPM - These require further silicon investigation